## Slide 1: Bearing Design
ME 313: Mechanical Design
Week 10

## Slide 2: Today’s Topics
Overview of Bearings
Rolling-contact bearings
  Principles of rolling contact bearings
  Type of rolling-contact bearings
  Bearing life
  Bearing reliability
Journal bearings
  Principles of journal bearings
  Theory of lubrication

## Slide 3: Bearing Uses
Device that allows constrained motions between two or more components

## Slide 4: Bearing Categories
Can be divided based on principles of operation or by allowed motions

## Slide 5: Bearing Types by Allowed Motions
Axial rotation
    Shaft rotation
Linear motion
    drawer
Spherical rotation
    Ball and socket joint (shoulder)
Hinged motion
    Door, elbow, knee, etc.

## Slide 6: Bearing Types by Principles of Operation
Plain bearing
Rolling-contact bearing
Fluid bearing
Jewel bearing
Magnetic bearing
Flexure bearing

## Slide 7: Main Focus
Rolling-contact bearings
Journal bearings

## Slide 8: Rolling Element Bearings
Bearing have rolling elements, which allows relative motions between two surfaces without sliding
Rolling elements can be:
    Balls
    Needles
    Cylinders (rollers)
    Tapered rollers

## Slide 9: Ball Bearings
Use to reduce rotational friction and support radial and axial loads

## Slide 10: Typical Construction of Ball Bearing
Angular Contact
    For radial and axial load
Axial
    Mainly for axial load
Deep groove
    Groove size is close to ball diameter, enhancing load resistance but limiting misalignment

## Slide 11: Roller/Needle Bearings
Rollers are cylinders with slightly longer length than diameter
Needles are cylindrical rollers but with small diameter and long

## Slide 12: Tapered Roller Bearings
Use to support large axial and radial load simultaneously
Rollers are tapered
    Each is a part of a cone
Notes: Cones that meet at a point can roll over each other without slipping

## Slide 13: Rolling Element Bearing Failure
There are 3 major failure modes
    Abrasion: heavy scratching on race surface
    Fatigue: race or ball fracture due to repeated contact stress
    Pressure-induced welding: metal bonding due to high pressure

## Slide 14: Bearing Life
Bearing life is usually defined by
    Number of revolutions of inner ring until first sign of failure
    Number of hours of use at standard angular speed
Rating life is a term used by most manufacturers
    number of revolutions or hours than 90% of bearings will achieve before failure develops, L10

## Slide 15: Bearing Load-Life Tradeoff at Constant Reliability
Data from regression shows that
    F is exerted load on bearing
    L is bearing life
      a = 3 for ball bearing
      a = 10/3 for roller bearings (cylindrical and tapered rollers)
Manufacturer choose to rate the load based on a set number of revolutions
    The rated load is usually called catalog load rating, C10

## Slide 16: Catalog Load Rating and Rating Life
We can relate load requirement to expected bearing life by
Also can be converted to number of revolutions
      L is life, in hours
      n is angular speed, rev/min
      Subscript:
        R for rated
        D for desired

## Slide 17: Example

## Slide 18: Bearing Survival: Reliability-Life Tradeoff
At constant load, the longer bearing works, the lower its chance to continue working
  follows a Weibull distribution
    R = reliability
    x = life
    x0 = guaranteed or minimum value of life
    theta = characteristic parameter
    b = shape parameter

## Slide 19: Load-Life-Reliability
Combine the two previous equations, we have

## Slide 20: Combined Radial and Thrust Loading
When there are both radial and thrust loads, equivalent load needs to be calculated to determine bearing life
    depends on relative axial to radial load and whether inner or outer ring is rotating

## Slide 21: General Form of Equivalent Load
General form can be written as
      V = 1 for inner ring rotates, = 1.2 for outer
      i = 1 when Fa/VFr < e and i = 2 when Fa/VFr > e
    dependent on axial load compared to basic static load rating C0
Fa/C0 | e | Fa/VFr < e |  | Fa/VFr > e | 
 |  | X1 | Y1 | X2 | Y2
0.014 | 0.19 | 1 | 0 | 0.56 | 2.30
0.028 | 0.22 | 1 | 0 | 0.56 | 1.99
0.07 | 0.27 | 1 | 0 | 0.56 | 1.63
0.17 | 0.34 | 1 | 0 | 0.56 | 1.31
0.56 | 0.44 | 1 | 0 | 0.56 | 1.00

## Slide 22: Example

## Slide 23: Journal Bearing
Make uses of lubrication to reduce friction
    no direct contact between two surfaces

## Slide 24: Types of Journal Bearings
Hydrostatically lubricated
    external pump is needed to keep lubricant correctly pressurized
Hydrodynamically lubricated
    lubricant is pressurized by the motion of surfaces

## Slide 25: Theory of Lubrication
Required to understand the basics of how journal bearing works
    Directly related to fluid mechanics

## Slide 26: Petroff’s Equation
Assuming concentric shaft and housing
      N is rotational speed (rev/s)
      r is shaft radius
      c is shaft-housing clearance
Torque on the shaft is

## Slide 27: Frictional Torque
Consider for W on bearing
    pressure on shaft projected area is
    frictional force is
    torque due to friction is

## Slide 28: Equivalent Coefficient of Friction
This is called Petroff’s equation
    provides quick estimates for coefficient of friction of lightly loaded bearing
Two important quantities to lubrication are

## Slide 29: Heat Generated in Journal Bearing
Constant shearing increases temperature of lubricant
    flow rate of lubricant through a clearance is
    Heat loss by convection and radiation is
    Heat generated is from frictional torque

## Slide 30: Lubricant Temperature
At steady state, heat generated is equal to heat loss
Lubricant temperature usually should not go above approximately 120 C
    unless lubricant manufacturer states a higher number

## Slide 31: Example