## Slide 1: Shafts, Axles, and Couplings
ME 313: Mechanical Design
Week 11

## Slide 2: Topics to Cover
Shafts and Axles
    Overview
    Strength considerations
    Speed considerations
Couplings
    Overview
    Pins and keys
    Tapered Couplings

## Slide 3: Shafts and Axles
Shafts
    transfer of torque or rotation from source to intended component(s)
Axle
    nonrotational component used to support rotational parts

## Slide 4: Typical Shaft Designs
To transmit power from driving device (motor or engine) to machine, gears, pulleys, flywheels, clutches, or sprockets are mounted on shaft
Torque is transmitted to shaft by press fit, keys, or pins
Shaft rotates usually on rolling contact bearing or journal bearing

## Slide 5: Typical Shaft Designs (Cont)
Retaining rings
    take axial load and retain shaft positions

## Slide 6: Strength Considerations
Shaft and axle are subjected to these loads
    bending
    torsion
    shear
We have to make sure shafts can take these combined loads to operate

## Slide 7: Bending Loads in Shafts
Transverse load away from fulcrum point causes bending
    radial load from gear
    belt tension from pulley
Resulting in bending stress

## Slide 8: Axial Loads on Shaft
Compressive/tensile load from axial load
    axial load from bevel or helical gear

## Slide 9: Torsional Loads in Shaft
Shear stress from torsional load

## Slide 10: Combined Loading on Shaft
In machine applications, shafts are usually subjected to combined loads
Use stress transformation to analyze stress
    principal stresses
    maximum shear stress

## Slide 11: Speed Consideration
When shaft is spinning, eccentricity causes centrifugal force deflection
    for simply supported shaft
    for clamped shaft
        m is mass per length
        l is length of shaft

## Slide 12: Example

## Slide 13: Couplings
Device used to transfer power from one shaft end to another
Can allow misalignment and end movement

## Slide 14: Rigid Couplings
Can transfer large power
no misalignment allowed
no backlash
example: muff couplings, clamp couplings, flange couplings

## Slide 15: Flexible Couplings
Misalignment (angle and radial) allowed
End movement allowed
Examples: universal coupling, bellow coupling, CV coupling, etc

## Slide 16: Keys and Keyways
small material inserted in slot to transfer torque between driving mechanism and shaft
shear stress in key is

## Slide 17: Pins
Used to locate shaft and transfer torque
  Shear stress in pin is due to torque T is
R
r

## Slide 18: Tapered Coupling
Used to fit a gear or rotating arm to a shaft
    by using taper, axial force is translated to radial force, generating friction
α

## Slide 19: Tapered Coupling Torque Capacity
Assuming uniform pressure
torque capacity depends on friction force
α
F
Pa
d
d

## Slide 20: Shaft Assembly General Rules
Shaft should be as short as possible
    small overhand
    minimize bending stress
    increase critical speed
Bearing support should be as farthest apart as possible
    provide highest stability